## Slide 1
GRT-Arm
Gesture Replication and Translation for Robotic Arm
Team Members
    Mohamed Omar
    Hamza Ehab
    Boshra Akram
    Farida Abdelbaky
    Mohamed Tarek

## Slide 2
Overview
This project integrates computer vision, machine learning, and robotics to create a system that combines real-time image processing, gesture recognition, serial communication, and precise robotic control to achieve seamless translation of visual inputs into physical outputs.

## Slide 3
Project Flow
Captures hand gestures using a webcam.
Processes and classifies gestures into corresponding letters (e.g., American Sign Language alphabet).
Sends the classified letter to an Arduino via serial communication.
Controls a robotic arm to mimic the gesture corresponding to the letter.
The letter is displayed on an LCD

## Slide 4
    7 Servo Motors
    Arduino UNO
    ESP8266
    bread boards
    3 batteries (3.7v each)
    Wires
    Buck Adapter
    LCD I2C
components used

## Slide 5
    OpenCV (cv2)
    MediaPipe
Computer Vision libraries :
    is an Open-source computer vision library used here for capturing video frames, image processing and displaying results.
    Is a framework, provides pre-built solutions for tasks like hand tracking, face detection, pose estimation, object detection, and more.

## Slide 7
ESP8266
The ESP uses WebSocket Protocol to receive data from another device wirelessly (e.g., a cell phone or computer) over the network and sends it to the Arduino.

## Slide 8
Arduino Uno
    The Arduino receives input data from the ESP module via Serial
    It processes the received data to translate the gesture to the matching letter.
    Based on the input, it sends precise control signals to the corresponding servo motor in the Robotic Arm.
    Each servo controls a specific finger of the robot arm, enabling coordinated movement.

## Slide 9
LCD I2C
The system incorporates an LCD I2C module to provide real-time feedback and enhance user interaction. This 16x2 LCD, interfaced via the I2C protocol, displays the recognized letter from the gesture recognition process, as well as the robotic arm’s status, such as "Gesture: A" .
This display offers a clear, immediate visual confirmation of the system’s operation, improving usability and debugging during gesture translation.
RoboTech

## Slide 10
Servo Motors
In the robotic arm, servo motors are pivotal for mimicking hand gestures, with each servo dedicated to controlling one finger. Each motor precisely adjusts the angle of its corresponding finger, enabling the arm to replicate specific letter gestures

## Slide 11
Batteries and Adapters
The robotic arm’s power system is driven by 3.7V batteries and a buck adapter to ensure reliable operation. These 3.7V batteries supply power to the servo motors and Arduino, providing the necessary energy for consistent gesture execution.

## Slide 12
Thank You ^^